## Slide 1: William Stallings Computer Organization and Architecture 6th Edition
Chapter 11
Instruction Sets:
Addressing Modes and Formats

## Slide 2: Addressing Modes
Immediate
Direct
Indirect
Register
Register Indirect
Displacement (Indexed)
Stack
Notes: 2

## Slide 3: Immediate Addressing
Operand is part of instruction
Operand = address field
e.g. ADD AX, 5h
LDA #5
  Add 5 to contents of accumulator
  5 is operand
No memory reference to fetch data
Fast
Limited range
Notes: 3

## Slide 4: Direct Addressing
Address field contains address of operand
Effective address EA = address field (A)
ADD AX, value
Value DB 05h
  Add contents of cell value to accumulator AX
  Look in memory at address value for operand
Single memory reference to access data
No additional calculations to work out effective address
Limited address space
Notes: 5

## Slide 5: Direct Addressing Diagram
Notes: 6

## Slide 6: Indirect Addressing (1/2)
Memory cell pointed to by address field contains the address of (pointer to) the operand
EA =(A)
  Look in A, find address (A) and look there for operand
e.g. ADD AX, (A)
  Add contents of cell pointed to by contents of A to accumulator
Notes: 7

## Slide 7: Indirect Addressing (2/2)
Large address space
2n where n = word length
May be nested, multilevel, cascaded
  e.g. EA = (((A)))
    Draw the diagram yourself
Multiple memory accesses to find operand
Hence slower
Notes: 8

## Slide 8: Indirect Addressing Diagram
Notes: 9

## Slide 9: Register Addressing (1/2)
Operand is held in register named in address filed
EA = R
Limited number of registers
Very small address field needed
  Shorter instructions
  Faster instruction fetch
  MOV AX, BX
  ADD AX, BX
Notes: 10

## Slide 10: Register Addressing (2/2)
No memory access
Very fast execution
Very limited address space
Multiple registers helps performance
  Requires good assembly programming or compiler writing
  N.B. C programming
    register int a;
c.f. Direct addressing
Notes: 11

## Slide 11: Register Addressing Diagram
Notes: 12

## Slide 12: Register Indirect Addressing
C.f. indirect addressing
EA = (R)
Operand is in memory cell pointed to by contents of register R
Large address space (2n)
One fewer memory access than indirect addressing
Notes: 13

## Slide 13: Register Indirect Addressing Diagram
Notes: 14

## Slide 14: Displacement Addressing
EA = A + (R)
Effective address=start address + displacement
Effective address=Offset + (Segment Register)
Use direct and register indirect
Address field hold two values
  A = base value
  R = register that holds displacement
  or vice versa
Notes: 15

## Slide 15: Displacement Addressing Diagram
Notes: 16

## Slide 16: Relative Addressing (PC-Relative)
A version of displacement addressing
R = Program counter, PC
EA = A + (PC)
i.e. get operand from A cells from current location pointed to by PC
c.f locality of reference & cache usage
Notes: 17

## Slide 17: Base-Register Addressing
A holds displacement
  EA = (CS) + A
R holds pointer to base address
R may be explicit or implicit
e.g. segment registers in 80x86
Notes: 18

## Slide 18: Indexed Addressing
A = base
R = displacement
  EA = A + (R)
Good for accessing arrays
  EA = A + (R)
  R++
Notes: 19

## Slide 19: Combinations
Postindex
  EA = (A) + (R)
Preindex
  EA = (A+(R))
Notes: 20

## Slide 20: Stack Addressing
Operand is (implicitly) on top of stack
e.g.
  ADD Pop top two items from stack and add and push
Notes: 21

## Slide 22: Pentium Addressing Modes
Virtual or effective address is offset into segment
  Starting address plus offset gives linear address
  This goes through page translation if paging enabled
9 addressing modes available
  Immediate
  Register operand
  Displacement
  Base
  Base with displacement
  Scaled index with displacement
  Base with index and displacement
  Base scaled index with displacement
  Relative

## Slide 23: Pentium Addressing Mode Calculation

## Slide 24: PowerPC Addressing Modes
Load/store architecture
  Indirect
    Instruction includes 16 bit displacement to be added to base register (may be GP register)
    Can replace base register content with new address
  Indirect indexed
    Instruction references base register and index register (both may be GP)
    EA is sum of contents
Branch address
  Absolute
  Relative
  Indirect
Arithmetic
  Operands in registers or part of instruction
  Floating point is register only

## Slide 25: PowerPC Memory Operand Addressing Modes

## Slide 26: Instruction Formats
Layout of bits in an instruction
Includes opcode
Includes (implicit or explicit) operand(s)
Usually more than one instruction format in an instruction set

## Slide 27: Instruction Length
Affected by and affects:
  Memory size
  Memory organization
  Bus structure
  CPU complexity
  CPU speed
Trade off between powerful instruction repertoire and saving space

## Slide 28: Allocation of Bits
Number of addressing modes
Number of operands
Register versus memory
Number of register sets
Address range
Address granularity

## Slide 29: Pentium Instruction Format

## Slide 30: PDP-8 Instruction Format

## Slide 31: PDP-10 Instruction Format

## Slide 32: PDP-11 Instruction Format

## Slide 33: VAX Instruction Examples

## Slide 34: PowerPC Instruction Formats (1)

## Slide 35: PowerPC Instruction Formats (2)