## Slide 1: Chapter 1. Basic Structure of Computers

## Slide 2: Functional Units

## Slide 3: Functional Units
Figure 1.1. Basic functional units of a computer.
I/O
Processor
Output
Memory
Input
and
Arithmetic
logic
Control

## Slide 4: Information Handled by a Computer
Instructions/machine instructions
Govern the transfer of information within a computer as well as between the computer and its I/O devices
Specify the arithmetic and logic operations to be performed
Program
Data
Used as operands by the instructions
Source program
Encoded in binary code – 0 and 1

## Slide 5: Memory Unit
Store programs and data
Two classes of storage
Primary storage
Fast
Programs must be stored in memory while they are being executed
Large number of semiconductor storage cells
Processed in words
Address
RAM and memory access time
Memory hierarchy – cache, main memory
Secondary storage – larger and cheaper

## Slide 6: Arithmetic and Logic Unit (ALU)
Most computer operations are executed in ALU of the processor.
Load the operands into memory – bring them to the processor – perform operation in ALU – store the result back to memory or retain in the processor.
Registers
Fast control of ALU

## Slide 7: Control Unit
All computer operations are controlled by the control unit.
The timing signals that govern the I/O transfers are also generated by the control unit.
Control unit is usually distributed throughout the machine instead of standing alone.
Operations of a computer:
Accept information in the form of programs and data through an input unit and store it in the memory
Fetch the information stored in the memory, under program control, into an ALU, where the information is processed
Output the processed information through an output unit
Control all activities inside the machine through a control unit

## Slide 8: The processor : Data Path and Control
Two types of functional units:
  elements that operate on data values (combinational)
  elements that contain state (state elements)

## Slide 9: Five Execution Steps
Step name | Action for R-type instructions | Action for Memory-reference Instructions | Action for branches | Action for jumps
Instruction fetch | IR = MEM[PC] PC = PC + 4 |  |  | 
Instruction decode/ register fetch | A = Reg[IR[25-21]] B = Reg[IR[20-16]] ALUOut = PC + (sign extend (IR[15-0])<<2) |  |  | 
Execution, address computation, branch/jump completion | ALUOut = A op B | ALUOut = A+sign extend(IR[15-0]) | IF(A==B) Then PC=ALUOut | PC=PC[31-28]¦¦(IR[25-0]<<2)
Memory access or R-type completion | Reg[IR[15-11]] = ALUOut | Load:MDR =Mem[ALUOut] or Store:Mem[ALUOut] = B |  | 
Memory read completion |  | Load: Reg[IR[20-16]] = MDR |  | 

## Slide 10: Basic Operational Concepts

## Slide 11: Review
Activity in a computer is governed by instructions.
To perform a task, an appropriate program consisting of a list of instructions is stored in the memory.
Individual instructions are brought from the memory into the processor, which executes the specified operations.
Data to be used as operands are also stored in the memory.

## Slide 12: A Typical Instruction
Add LOCA, R0
Add the operand at memory location LOCA to the operand in a register R0 in the processor.
Place the sum into register R0.
The original contents of LOCA are preserved.
The original contents of R0 is overwritten.
Instruction is fetched from the memory into the processor – the operand at LOCA is fetched and added to the contents of R0 – the resulting sum is stored in register R0.

## Slide 13: Separate Memory Access and ALU Operation
Load LOCA, R1
Add R1, R0
Whose contents will be overwritten?

## Slide 14: Connection Between the Processor and the Memory

## Slide 15: Registers
Instruction register (IR)
Program counter (PC)
General-purpose register (R0 – Rn-1)
Memory address register (MAR)
Memory data register (MDR)

## Slide 16: Typical Operating Steps
Programs reside in the memory through input devices
PC is set to point to the first instruction
The contents of PC are transferred to MAR
A Read signal is sent to the memory
The first instruction is read out and loaded into MDR
The contents of MDR are transferred to IR
Decode and execute the instruction

## Slide 17: Typical Operating Steps (Cont’)
Get operands for ALU
  General-purpose register
  Memory (address to MAR – Read – MDR to ALU)
Perform operation in ALU
Store the result back
  To general-purpose register
  To memory (address to MAR, result to MDR – Write)
During the execution, PC is incremented to the next instruction

## Slide 18: Interrupt
Normal execution of programs may be preempted if some device requires urgent servicing.
The normal execution of the current program must be interrupted – the device raises an interrupt signal.
Interrupt-service routine
Current system information backup and restore (PC, general-purpose registers, control information, specific information)

## Slide 19: Bus Structures
There are many ways to connect different parts inside a computer together.
A group of lines that serves as a connecting path for several devices is called a bus.
Address/data/control

## Slide 20: Bus Structure
Single-bus

## Slide 21: Speed Issue
Different devices have different transfer/operate speed.
If the speed of bus is bounded by the slowest device connected to it, the efficiency will be very low.
How to solve this?
A common approach – use buffers.

## Slide 22: Performance

## Slide 23: Performance
The most important measure of a computer is how quickly it can execute programs.
Three factors affect performance:
Hardware design
Instruction set
Compiler

## Slide 24: Performance
Processor time to execute a program depends on the hardware involved in the execution of individual machine instructions.
Main
memory
Processor
Bus
Cache
memory
Figure 1.5.
The processor cache.

## Slide 25: Performance
The processor and a relatively small cache memory can be fabricated on a single integrated circuit chip.
Speed
Cost
Memory management

## Slide 26: Processor Clock
Clock, clock cycle, and clock rate
The execution of each instruction is divided into several steps, each of which completes in one clock cycle.
Hertz – cycles per second

## Slide 27: Basic Performance Equation
T – processor time required to execute a program that has been prepared in high-level language
N – number of actual machine language instructions needed to complete the execution (note: loop)
S – average number of basic steps needed to execute one machine instruction. Each step completes in one clock cycle
R – clock rate
Note: these are not independent to each other
How to improve T?

## Slide 28: Pipeline and Superscalar Operation
Instructions are not necessarily executed one after another.
The value of S doesn’t have to be the number of clock cycles to execute one instruction.
Pipelining – overlapping the execution of successive instructions.
Add R1, R2, R3
Superscalar operation – multiple instruction pipelines are implemented in the processor.
Goal – reduce S (could become <1!)

## Slide 29: Clock Rate
Increase clock rate
Improve the integrated-circuit (IC) technology to make the circuits faster
Reduce the amount of processing done in one basic step (however, this may increase the number of basic steps needed)
Increases in R that are entirely caused by improvements in IC technology affect all aspects of the processor’s operation equally except the time to access the main memory.

## Slide 30: CISC and RISC
Tradeoff between N and S
A key consideration is the use of pipelining
S is close to 1 even though the number of basic steps per instruction may be considerably larger
It is much easier to implement efficient pipelining in processor with simple instruction sets
Reduced Instruction Set Computers (RISC)
Complex Instruction Set Computers (CISC)

## Slide 31: Compiler
A compiler translates a high-level language program into a sequence of machine instructions.
To reduce N, we need a suitable machine instruction set and a compiler that makes good use of it.
Goal – reduce N×S
A compiler may not be designed for a specific processor; however, a high-quality compiler is usually designed for, and with, a specific processor.

## Slide 32: Performance Measurement
T is difficult to compute.
Measure computer performance using benchmark programs.
System Performance Evaluation Corporation (SPEC) selects and publishes representative application programs for different application domains, together with test results for many commercially available computers.
Compile and run (no simulation)
Reference computer

## Slide 33: Multiprocessors and Multicomputers
Multiprocessor computer
Execute a number of different application tasks in parallel
Execute subtasks of a single large task in parallel
All processors have access to all of the memory – shared-memory multiprocessor
Cost – processors, memory units, complex interconnection networks
Multicomputers
Each computer only have access to its own memory
Exchange message via a communication network – message-passing multicomputers

## Slide 35: Chapter 2. Machine Instructions and Programs
Notes: <number>

## Slide 36: Objectives
Machine instructions and program execution, including branching and subroutine call and return operations.
Number representation and addition/subtraction in the 2’s-complement system.
Addressing methods for accessing register and memory operands.
Assembly language for representing machine instructions, data, and programs.
Program-controlled Input/Output operations.
Notes: <number>

## Slide 37: Number, Arithmetic Operations, and Characters
Notes: <number>

## Slide 38: Signed Integer
3 major representations:
Sign and magnitude
One’s complement
Two’s complement
Assumptions:
4-bit machine word
16 different values can be represented
Roughly half are positive, half are negative
Notes: <number>

## Slide 39: Sign and Magnitude Representation
High order bit is sign: 0 = positive (or zero), 1 = negative
Three low order bits is the magnitude: 0 (000) thru 7 (111)
Number range for n bits = +/-2n-1 -1
Two representations for 0
Notes: <number>

## Slide 40: One’s Complement Representation
Subtraction implemented by addition & 1's complement
Still two representations of 0! This causes some problems
Some complexities in addition
Notes: <number>

## Slide 41: Two’s Complement Representation
Only one representation for 0
One more negative number than positive number
like 1's comp
except shifted
one position
clockwise
Notes: <number>

## Slide 42: Binary, Signed-Integer Representations
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
0
0
1
1
0
0
0
0
1
1
0
0
1
1
1
0
1
0
1
0
1
0
0
1
0
1
0
1
0
1
1
+
1
-
2
+
3
+
4
+
5
+
6
+
7
+
2
-
3
-
4
-
5
-
6
-
7
-
8
-
0
+
0
-
1
+
2
+
3
+
4
+
5
+
6
+
7
+
0
+
7
-
6
-
5
-
4
-
3
-
2
-
1
-
0
-
1
+
2
+
3
+
4
+
5
+
6
+
7
+
0
+
7
-
6
-
5
-
4
-
3
-
2
-
1
-
b
3
b
2
b
1
b
0
Sign and
magnitude
1'
s complement
2'
s complement
B
V
alues represented
Figure 2.1. Binary, signed-integer representations.
Page 28
Notes: <number>

## Slide 43: Addition and Subtraction – 2’s Complement
4
+ 3
7
0100
0011
0111
-4
+ (-3)
-7
1100
1101
11001
4
- 3
1
0100
1101
10001
-4
+ 3
-1
1100
0011
1111
If carry-in to the high
order bit =
carry-out then ignore
carry
if carry-in differs from
carry-out then overflow
Simpler addition scheme makes twos complement the most common
choice for integer number systems within digital systems
Notes: <number>

## Slide 44: 2’s-Complement Add and Subtract Operations
1 1 0 1
0 1 1 1
0 1 0 0
0 0 1 0
1 1 0 0
1 1 1 0
0 1 1 0
1 1 0 1
0 0 1 1
1 0 0 1
0 1 0 1
1 1 1 0
1 0 0 1
1 1 1 1
1 0 0 0
0 0 1 0
0 0 1 1
0 1 0 1
4
+
(
)
2
-


3
+
(
)
2
-


8
-


5
+
(
)
+
+
+
+
+
+
1 1 1 0
0 1 0 0
1 0 1 0
0 1 1 1
1 1 0 1
0 1 0 0
6
-


2
-


4
+
(
)
3
-


4
+
(
)
7
+
(
)
+
+
(b)
(d)
1 0 1 1
1 1 1 0
1 0 0 1
1 1 0 1
1 0 0 1
0 0 1 0
0 1 0 0
0 1 1 0
0 0 1 1
1 0 0 1
1 0 1 1
1 0 0 1
0 0 0 1
0 0 1 0
1 1 0 1
0 1 0 1
0 0 1 0
0 0 1 1
5
-


2
+
(
)
3
+
(
)
5
+
(
)
2
+
(
)
4
+
(
)
2
-


7
-


3
-


7
-


6
+
(
)
3
+
(
)
1
+
(
)
7
-


5
-


7
-


2
+
(
)
3
-


+
+
-
-
-
-
-
-
(a)
(c)
(e)
(f)
(g)
(h)
(i)
(j)
Figure 2.4. 2's-complement Add and Subtract operations.
Page 31
Notes: <number>

## Slide 45: Overflow - Add two positive numbers to get a negative number or two negative numbers to get a positive number
5 + 3 = -8
-7 - 2 = +7
0000
0001
0010
0011
1000
0101
0110
0100
1001
1010
1011
1100
1101
0111
1110
1111
+0
+1
+2
+3
+4
+5
+6
+7
-8
-7
-6
-5
-4
-3
-2
-1
0000
0001
0010
0011
1000
0101
0110
0100
1001
1010
1011
1100
1101
0111
1110
1111
+0
+1
+2
+3
+4
+5
+6
+7
-8
-7
-6
-5
-4
-3
-2
-1
Notes: <number>

## Slide 46: Overflow Conditions
5
3
-8
0 1 1 1
0 1 0 1
0 0 1 1
1 0 0 0
-7
-2
7
1 0 0 0
1 0 0 1
1 1 0 0
1 0 1 1 1
5
2
7
0 0 0 0
0 1 0 1
0 0 1 0
0 1 1 1
-3
-5
-8
1 1 1 1
1 1 0 1
1 0 1 1
1 1 0 0 0
Overflow
Overflow
No overflow
No overflow
Overflow when carry-in to the high-order bit does not equal carry out
Notes: <number>

## Slide 47: Sign Extension
Task:
  Given w-bit signed integer x
  Convert it to w+k-bit integer with same value
Rule:
  Make k copies of sign bit:
  X  = xw–1 ,…, xw–1 , xw–1 , xw–2 ,…, x0
k copies of MSB
• • •
X
X 
• • •
• • •
• • •
w
w
k
Notes: <number>

## Slide 48: Sign Extension Example
short int x = 15213;
int ix = (int) x;
short int y = -15213;
int iy = (int) y;
Notes: <number>

## Slide 49: Memory Locations, Addresses, and Operations
Notes: <number>

## Slide 50: Memory Location, Addresses, and Operation
Memory consists of many millions of storage cells, each of which can store 1 bit.
Data is usually accessed in n-bit groups. n is called word length.
second word
first word
Figure 2.5. Memory words.
n
bits
last word
i
th word
•
•
•
•
•
•
Notes: <number>

## Slide 51: Memory Location, Addresses, and Operation
32-bit word length example
(b) Four characters
character
character
character
character
(a) A signed integer
Sign bit:
for positive numbers
for negative numbers
ASCII
ASCII
ASCII
ASCII
32 bits
8 bits
8 bits
8 bits
8 bits
b
31
b
30
b
1
b
0
b
31
0
=
b
31
1
=
•
•
•
Notes: <number>

## Slide 52: Memory Location, Addresses, and Operation
To retrieve information from memory, either for one word or one byte (8-bit), addresses for each location are needed.
A k-bit address memory has 2k memory locations, namely 0 – 2k-1, called memory space.
24-bit memory: 224 = 16,777,216 = 16M (1M=220)
32-bit memory: 232 = 4G (1G=230)
1K(kilo)=210
1T(tera)=240
Notes: <number>

## Slide 53: Memory Location, Addresses, and Operation
It is impractical to assign distinct addresses to individual bit locations in the memory.
The most practical assignment is to have successive addresses refer to successive byte locations in the memory – byte-addressable memory.
Byte locations have addresses 0, 1, 2, … If word length is 32 bits, they successive words are located at addresses 0, 4, 8,…
Notes: <number>

## Slide 54: Big-Endian and Little-Endian Assignments
2
k
4
-
2
k
3
-
2
k
2
-
2
k
1
-
2
k
4
-
2
k
4
-
0
1
2
3
4
5
6
7
0
0
4
2
k
1
-
2
k
2
-
2
k
3
-
2
k
4
-
3
2
1
0
7
6
5
4
Byte address
Byte address
(a) Big-endian assignment
(b) Little-endian assignment
4
W
ord
address
•
•
•
•
•
•
Figure 2.7. Byte and word addressing.
Big-Endian: lower byte addresses are used for the most significant bytes of the word
Little-Endian: opposite ordering. lower byte addresses are used for the less significant bytes of the word
Notes: <number>

## Slide 55: Memory Location, Addresses, and Operation
Address ordering of bytes
Word alignment
  Words are said to be aligned in memory if they begin at a byte addr. that is a multiple of the num of bytes in a word.
    16-bit word: word addresses: 0, 2, 4,….
    32-bit word: word addresses: 0, 4, 8,….
    64-bit word: word addresses: 0, 8,16,….
Access numbers, characters, and character strings
Notes: <number>

## Slide 56: Memory Operation
Load (or Read or Fetch)
Copy the content. The memory content doesn’t change.
Address – Load
Registers can be used
Store (or Write)
Overwrite the content in memory
Address and Data – Store
Registers can be used
Notes: <number>

## Slide 57: Instruction and Instruction Sequencing
Notes: <number>

## Slide 58: “Must-Perform” Operations
Data transfers between the memory and the processor registers
Arithmetic and logic operations on data
Program sequencing and control
I/O transfers
Notes: <number>

## Slide 59: Register Transfer Notation
Identify a location by a symbolic name standing for its hardware binary address (LOC, R0,…)
Contents of a location are denoted by placing square brackets around the name of the location (R1←[LOC], R3 ←[R1]+[R2])
Register Transfer Notation (RTN)
Notes: <number>

## Slide 60: Assembly Language Notation
Represent machine instructions and programs.
Move LOC, R1 = R1←[LOC]
Add R1, R2, R3 = R3 ←[R1]+[R2]
Notes: <number>

## Slide 61: CPU Organization
Single Accumulator
  Result usually goes to the Accumulator
  Accumulator has to be saved to memory quite often
General Register
  Registers hold operands thus reduce memory traffic
  Register bookkeeping
Stack
  Operands and result are always in the stack

## Slide 62: Instruction Formats
Three-Address Instructions
  ADD R1, R2, R3 R1 ← R2 + R3
Two-Address Instructions
  ADD R1, R2 R1 ← R1 + R2
One-Address Instructions
  ADD M AC ← AC + M[AR]
Zero-Address Instructions
  ADD TOS ← TOS + (TOS – 1)
RISC Instructions
  Lots of registers. Memory is restricted to Load & Store
Instruction
Opcode
Operand(s) or Address(es)

## Slide 63: Instruction Formats
Example: Evaluate (A+B)  (C+D)
Three-Address
  ADD R1, A, B ; R1 ← M[A] + M[B]
  ADD R2, C, D ; R2 ← M[C] + M[D]
  MUL X, R1, R2 ; M[X] ← R1  R2

## Slide 64: Instruction Formats
Example: Evaluate (A+B)  (C+D)
Two-Address
  MOV R1, A ; R1 ← M[A]
  ADD R1, B ; R1 ← R1 + M[B]
  MOV R2, C ; R2 ← M[C]
  ADD R2, D ; R2 ← R2 + M[D]
  MUL R1, R2 ; R1 ← R1  R2
  MOV X, R1 ; M[X] ← R1

## Slide 65: Instruction Formats
Example: Evaluate (A+B)  (C+D)
One-Address
  LOAD A ; AC ← M[A]
  ADD B ; AC ← AC + M[B]
  STORE T ; M[T] ← AC
  LOAD C ; AC ← M[C]
  ADD D ; AC ← AC + M[D]
  MUL T ; AC ← AC  M[T]
  STORE X ; M[X] ← AC

## Slide 66: Instruction Formats
Example: Evaluate (A+B)  (C+D)
Zero-Address
  PUSH A ; TOS ← A
  PUSH B ; TOS ← B
  ADD ; TOS ← (A + B)
  PUSH C ; TOS ← C
  PUSH D ; TOS ← D
  ADD ; TOS ← (C + D)
  MUL ; TOS ← (C+D)(A+B)
  POP X ; M[X] ← TOS

## Slide 67: Instruction Formats
Example: Evaluate (A+B)  (C+D)
RISC
  LOAD R1, A ; R1 ← M[A]
  LOAD R2, B ; R2 ← M[B]
  LOAD R3, C ; R3 ← M[C]
  LOAD R4, D ; R4 ← M[D]
  ADD R1, R1, R2 ; R1 ← R1 + R2
  ADD R3, R3, R4 ; R3 ← R3 + R4
  MUL R1, R1, R3 ; R1 ← R1  R3
  STORE X, R1 ; M[X] ← R1

## Slide 68: Using Registers
Registers are faster
Shorter instructions
  The number of registers is smaller (e.g. 32 registers need 5 bits)
Potential speedup
Minimize the frequency with which data is moved back and forth between the memory and processor registers.
Notes: <number>

## Slide 69: Instruction Execution and Straight-Line Sequencing
R0,C
B,R0
A,R0
Move
i
+ 8
Begin execution here
Move
i
Contents
Address
C
B
A
the program
Data for
segment
program
3-instruction
Add
i
+ 4
Figure 2.8. A program for C +
Assumptions:
- One memory operand
per instruction
- 32-bit word length
- Memory is byte
addressable
- Full memory address
can be directly specified
in a single-word instruction
Two-phase procedure
Instruction fetch
Instruction execute
Page 43
Notes: <number>

## Slide 70: Branching
NUM
n
NUM2
NUM1
R0,SUM
NUM
n
,R0
NUM3,R0
NUM2,R0
NUM1,R0
Figure 2.9. A straight-line program for adding n numbers.
Add
Add
Move
SUM
i
Move
Add
i
4
n
+
i
4
n
4
-
+
i
8
+
i
4
+
•
•
•
•
•
•
•
•
•
Notes: <number>

## Slide 71: Branching
N,R1
Move
NUM
n
NUM2
NUM1
R0,SUM
R1
"Next" number to R0
Figure 2.10. Using a loop to add n numbers.
LOOP
Decrement
Move
LOOP
loop
Program
Determine address of
"Next" number and add
N
SUM
n
R0
Clear
Branch>0
•
•
•
•
•
•
Branch target
Conditional branch
Notes: <number>

## Slide 72: Condition Codes
Condition code flags
Condition code register / status register
N (negative)
Z (zero)
V (overflow)
C (carry)
Different instructions affect different flags
Notes: <number>

## Slide 73: Conditional Branch Instructions
Example:
  A: 1 1 1 1 0 0 0 0
  B: 0 0 0 1 0 1 0 0
A: 1 1 1 1 0 0 0 0
+(−B): 1 1 1 0 1 1 0 0
1 1 0 1 1 1 0 0
C = 1
S = 1
V = 0
Z = 0

## Slide 74: Status Bits
ALU
V
Z
S
C
Zero Check
Cn
Cn-1
Fn-1
A
B
F

## Slide 75: Addressing Modes
Notes: <number>

## Slide 76: Generating Memory Addresses
How to specify the address of branch target?
Can we give the memory operand address directly in a single Add instruction in the loop?
Use a register to hold the address of NUM1; then increment by 4 on each pass through the loop.
Notes: <number>

## Slide 77: Addressing Modes
Implied
  AC is implied in “ADD M[AR]” in “One-Address” instr.
  TOS is implied in “ADD” in “Zero-Address” instr.
Immediate
  The use of a constant in “MOV R1, 5”, i.e. R1 ← 5
Register
  Indicate which register holds the operand
Instruction
Opcode
Mode
...

## Slide 78: Addressing Modes
Register Indirect
  Indicate the register that holds the number of the register that holds the operand
    MOV R1, (R2)
Autoincrement / Autodecrement
  Access & update in 1 instr.
Direct Address
  Use the given address to access a memory location
R1
R2 = 3
R3 = 5

## Slide 79: Addressing Modes
Indirect Address
  Indicate the memory location that holds the address of the memory location that holds the data
AR = 101
100
101
102
103
104
Memory
0 1 0 4
1 1 0 A

## Slide 80: Addressing Modes
100
101
102
103
104
Memory
0
1
2
Relative Address
  EA = PC + Relative Addr
AR = 100
1 1 0 A
PC = 2
+
Program
Data
Could be Positive or Negative (2’s Complement)

## Slide 81: Addressing Modes
Indexed
  EA = Index Register + Relative Addr
100
101
102
103
104
Memory
AR = 100
1 1 0 A
XR = 2
+
Could be Positive or Negative (2’s Complement)
Useful with “Autoincrement” or “Autodecrement”

## Slide 82: Addressing Modes
Base Register
  EA = Base Register + Relative Addr
100
101
102
103
104
Memory
BR = 100
0 0 0 A
AR = 2
+
Could be Positive or Negative (2’s Complement)
Usually points to the beginning of an array
0 0 0 5
0 0 1 2
0 1 0 7
0 0 5 9

## Slide 83: Addressing Modes
The different ways in which the location of an operand is specified in an instruction are referred to as addressing modes.
Name
Assem
bler
syn
tax
Addressing
function
Immediate
#V
alue
Op
erand
=
V
alue
Register
R
i
EA
=
R
i
Absolute
(Direct)
LOC
EA
=
LOC
Indirect
(R
i
)
EA
=
[R
i
]
(LOC)
EA
=
[LOC]
Index
X(R
i
)
EA
=
[R
i
]
+
X
Base
with
index
(R
i
,R
j
)
EA
=
[R
i
]
+
[R
j
]
Base
with
index
X(R
i
,R
j
)
EA
=
[R
i
]
+
[R
j
]
+
X
and
offset
Relative
X(PC)
EA
=
[PC]
+
X
Autoincremen
t
(R
i
)+
EA
=
[R
i
]
;
Incremen
t
R
i
Autodecrement
(R
i
)
Decremen
t
R
i
;
EA
=
[R
i
]

Notes: <number>

## Slide 84: Indexing and Arrays
Index mode – the effective address of the operand is generated by adding a constant value to the contents of a register.
Index register
X(Ri): EA = X + [Ri]
The constant X may be given either as an explicit number or as a symbolic name representing a numerical value.
If X is shorter than a word, sign-extension is needed.
Notes: <number>

## Slide 85: Indexing and Arrays
In general, the Index mode facilitates access to an operand whose location is defined relative to a reference point within the data structure in which the operand appears.
Several variations: (Ri, Rj): EA = [Ri] + [Rj] X(Ri, Rj): EA = X + [Ri] + [Rj]
Notes: <number>

## Slide 86: Relative Addressing
Relative mode – the effective address is determined by the Index mode using the program counter in place of the general-purpose register.
X(PC) – note that X is a signed number
Branch>0 LOOP
This location is computed by specifying it as an offset from the current value of PC.
Branch target may be either before or after the branch instruction, the offset is given as a singed num.
Notes: <number>

## Slide 87: Additional Modes
Autoincrement mode – the effective address of the operand is the contents of a register specified in the instruction. After accessing the operand, the contents of this register are automatically incremented to point to the next item in a list.
(Ri)+. The increment is 1 for byte-sized operands, 2 for 16-bit operands, and 4 for 32-bit operands.
Autodecrement mode: -(Ri) – decrement first
R0
Clear
R0,SUM
R1
(R2)+,R0
Figure 2.16. The Autoincrement addressing mode used in the program of Figure 2.12.
Initialization
Move
LOOP
Add
Decrement
LOOP
#NUM1,R2
N,R1
Move
Move
Branch>0
Notes: <number>

## Slide 88: Assembly Language
Notes: <number>

## Slide 89: Types of Instructions
Data Transfer Instructions
Name | Mnemonic
Load | LD
Store | ST
Move | MOV
Exchange | XCH
Input | IN
Output | OUT
Push | PUSH
Pop | POP
Data value is not modified

## Slide 90: Data Transfer Instructions
Mode | Assembly | Register Transfer
Direct address | LD ADR | AC ← M[ADR]
Indirect address | LD @ADR | AC ← M[M[ADR]]
Relative address | LD $ADR | AC ← M[PC+ADR]
Immediate operand | LD #NBR | AC ← NBR
Index addressing | LD ADR(X) | AC ← M[ADR+XR]
Register | LD R1 | AC ← R1
Register indirect | LD (R1) | AC ← M[R1]
Autoincrement | LD (R1)+ | AC ← M[R1], R1 ← R1+1

## Slide 91: Data Manipulation Instructions
Arithmetic
Logical & Bit Manipulation
Shift
Name | Mnemonic
Increment | INC
Decrement | DEC
Add | ADD
Subtract | SUB
Multiply | MUL
Divide | DIV
Add with carry | ADDC
Subtract with borrow | SUBB
Negate | NEG
Name | Mnemonic
Clear | CLR
Complement | COM
AND | AND
OR | OR
Exclusive-OR | XOR
Clear carry | CLRC
Set carry | SETC
Complement carry | COMC
Enable interrupt | EI
Disable interrupt | DI
Name | Mnemonic
Logical shift right | SHR
Logical shift left | SHL
Arithmetic shift right | SHRA
Arithmetic shift left | SHLA
Rotate right | ROR
Rotate left | ROL
Rotate right through carry | RORC
Rotate left through carry | ROLC

## Slide 92: Program Control Instructions
Name | Mnemonic
Branch | BR
Jump | JMP
Skip | SKP
Call | CALL
Return | RET
Compare (Subtract) | CMP
Test (AND) | TST
Subtract A – B but don’t store the result
1
0
1
1
0
0
0
1
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
Mask

## Slide 93: Conditional Branch Instructions
Mnemonic | Branch Condition | Tested Condition
BZ | Branch if zero | Z = 1
BNZ | Branch if not zero | Z = 0
BC | Branch if carry | C = 1
BNC | Branch if no carry | C = 0
BP | Branch if plus | S = 0
BM | Branch if minus | S = 1
BV | Branch if overflow | V = 1
BNV | Branch if no overflow | V = 0

## Slide 94: Basic Input/Output Operations
Notes: <number>

## Slide 95: I/O
The data on which the instructions operate are not necessarily already stored in memory.
Data need to be transferred between processor and outside world (disk, keyboard, etc.)
I/O operations are essential, the way they are performed can have a significant effect on the performance of the computer.
Notes: <number>

## Slide 96: Program-Controlled I/O Example
Read in character input from a keyboard and produce character output on a display screen.
Rate of data transfer (keyboard, display, processor)
Difference in speed between processor and I/O device creates the need for mechanisms to synchronize the transfer of data.
A solution: on output, the processor sends the first character and then waits for a signal from the display that the character has been received. It then sends the second character. Input is sent from the keyboard in a similar way.
Notes: <number>

## Slide 97: Program-Controlled I/O Example
- Registers
Flags
- Device interface
Notes: <number>

## Slide 98: Program-Controlled I/O Example
Machine instructions that can check the state of the status flags and transfer data: READWAIT Branch to READWAIT if SIN = 0 Input from DATAIN to R1 WRITEWAIT Branch to WRITEWAIT if SOUT = 0 Output from R1 to DATAOUT
Notes: <number>

## Slide 99: Program-Controlled I/O Example
Memory-Mapped I/O – some memory address values are used to refer to peripheral device buffer registers. No special instructions are needed. Also use device status registers. READWAIT Testbit #3, INSTATUS Branch=0 READWAIT MoveByte DATAIN, R1
Notes: <number>

## Slide 100: Program-Controlled I/O Example
Assumption – the initial state of SIN is 0 and the initial state of SOUT is 1.
Any drawback of this mechanism in terms of efficiency?
  Two wait loopsprocessor execution time is wasted
Alternate solution?
  Interrupt
Notes: <number>

## Slide 101: Stacks
Notes: <number>

## Slide 102: Home Work
For each Addressing modes mentioned before, state one example for each addressing mode stating the specific benefit for using such addressing mode for such an application.

## Slide 103: Stack Organization
SP
Stack Bottom
Current Top of Stack TOS
LIFO
  Last In First Out
0
1
2
3
4
7
8
9
10
5
6
Stack
0 0 5 5
0 0 0 8
0 0 2 5
0 0 1 5
0 1 2 3
FULL
EMPTY
DR

## Slide 104: Stack Organization
SP
Stack Bottom
Current Top of Stack TOS
PUSH
  SP ← SP – 1
  M[SP] ← DR
  If (SP = 0) then (FULL ← 1)
  EMPTY ← 0
0
1
2
3
4
7
8
9
10
5
6
Stack
0 0 5 5
0 0 0 8
0 0 2 5
0 0 1 5
0 1 2 3
FULL
EMPTY
1 6 9 0
1 6 9 0
DR
Current Top of Stack TOS

## Slide 105: Stack Organization
SP
Stack Bottom
Current Top of Stack TOS
POP
  DR ← M[SP]
  SP ← SP + 1
  If (SP = 11) then (EMPTY ← 1)
  FULL ← 0
0
1
2
3
4
7
8
9
10
5
6
Stack
0 0 5 5
0 0 0 8
0 0 2 5
0 0 1 5
0 1 2 3
FULL
EMPTY
1 6 9 0
DR
1 6 9 0
Current Top of Stack TOS

## Slide 106: Stack Organization
0
1
2
102
202
201
200
100
101
Memory Stack
  PUSH
    SP ← SP – 1
    M[SP] ← DR
  POP
    DR ← M[SP]
    SP ← SP + 1
Memory
PC
AR
SP
Program
Data
Stack

## Slide 107: Reverse Polish Notation
Infix Notation
  A + B
Prefix or Polish Notation
  + A B
Postfix or Reverse Polish Notation (RPN)
  A B +
A  B + C  D
A B  C D  +
RPN
(2) (4)  (3) (3)  +
(8) (3) (3)  +
(8) (9) +
17

## Slide 108: Reverse Polish Notation
Example
  (A + B)  [C  (D + E) + F]
(A B +)
(D E +)
C 

F +

## Slide 109: Reverse Polish Notation
Stack Operation
  (3) (4)  (5) (6)  +
PUSH 3
PUSH 4
MULT
PUSH 5
PUSH 6
MULT
ADD
3
4
12
5
6
30
42

## Slide 110: Additional Instructions
Notes: <number>

## Slide 111: Logical Shifts
Logical shift – shifting left (LShiftL) and shifting right (LShiftR)
C
R0
0
before:
after:
0
1
0
0
0
1
1
1
.
.
.
1
1
0
0
1
1
1
0
0
0
(b) Logical shift r
ight
LShiftR #2,R0
(a) Logical shift left
LShiftL #2,R0
C
R0
0
before:
after:
0
1
0
0
0
1
1
1
.
.
.
1
1
1
1
0
.
.
.
0
0
1
0
1
.
.
.
Notes: <number>

## Slide 112: Arithmetic Shifts
C
before:
after:
0
1
1
1
0
0
0
1
.
.
.
0
1
1
1
0
0
1
0
1
1
(c) Ar
ithmetic shift r
ight
AShiftR #2,R0
R0
.
.
.
Notes: <number>

## Slide 113: Rotate
Figure 2.32. Rotate instructions.
C
R0
before:
after:
0
1
0
0
0
1
1
1
.
.
.
1
1
1
0
1
1
1
0
0
1
(c) Rotate r
ight without carr
y
RotateR #2,R0
(a) Rotate left without carr
y
RotateL #2,R0
C
R0
before:
after:
0
1
0
0
0
1
1
1
.
.
.
1
1
1
1
0
.
.
.
1
0
1
0
1
C
before:
after:
0
1
0
0
0
1
1
1
.
.
.
1
1
1
0
1
1
1
0
0
0
(d) Rotate r
ight with carr
y
RotateRC #2,R0
R0
.
.
.
.
.
.
(b) Rotate left with carr
y
RotateLC #2,R0
C
R0
before:
after:
0
1
0
0
0
1
1
1
.
.
.
1
1
1
1
0
.
.
.
0
0
1
0
1
Notes: <number>

## Slide 114: Multiplication and Division
Not very popular (especially division)
Multiply Ri, Rj Rj ← [Ri] х [Rj]
2n-bit product case: high-order half in R(j+1)
Divide Ri, Rj Rj ← [Ri] / [Rj]
  Quotient is in Rj, remainder may be placed in R(j+1)
Notes: <number>

## Slide 115: Encoding of Machine Instructions
Notes: <number>

## Slide 116: Encoding of Machine Instructions
Assembly language program needs to be converted into machine instructions. (ADD = 0100 in ARM instruction set)
In the previous section, an assumption was made that all instructions are one word in length.
OP code: the type of operation to be performed and the type of operands used may be specified using an encoded binary pattern
Suppose 32-bit word length, 8-bit OP code (how many instructions can we have?), 16 registers in total (how many bits?), 3-bit addressing mode indicator.
Add R1, R2
Move 24(R0), R5
LshiftR #2, R0
Move #$3A, R1
Branch>0 LOOP
OP code
Source
Dest
Other info
8
7
7
10
(a) One-word instruction
Notes: <number>

## Slide 117: Encoding of Machine Instructions
What happens if we want to specify a memory operand using the Absolute addressing mode?
Move R2, LOC
14-bit for LOC – insufficient
Solution – use two words
(b) Two-word instruction
Memory address/Immediate operand
OP code
Source
Dest
Other info
Notes: <number>

## Slide 118: Encoding of Machine Instructions
Then what if an instruction in which two operands can be specified using the Absolute addressing mode?
Move LOC1, LOC2
Solution – use two additional words
This approach results in instructions of variable length. Complex instructions can be implemented, closely resembling operations in high-level programming languages – Complex Instruction Set Computer (CISC)
Notes: <number>

## Slide 119: Encoding of Machine Instructions
If we insist that all instructions must fit into a single 32-bit word, it is not possible to provide a 32-bit address or a 32-bit immediate operand within the instruction.
It is still possible to define a highly functional instruction set, which makes extensive use of the processor registers.
Add R1, R2 ----- yes
Add LOC, R2 ----- no
Add (R3), R2 ----- yes
Notes: <number>