## Slide 1: Nanoprogramming

## Slide 2: Introduction
In conventional microprogrammed computers each instruction fetched from main memory is interpreted by micro program stored in a single control memory CM.
The micro instructions do not directly issue the signals that control the hardware.
They are used to access a second control memory termed a nano control memory nCM,that directly controls the hardware.
2 LEVELS OF CONTROL MEMORY
Microcontrolled memory- higher level
Nanocontrol memory(Nanoinstructions)-lower level

## Slide 3
μPC
Micro control
Memory (μcm)
Microinstruction
Register μIR
μPC
Nano control
Memory (μcm)
Nanoinstruction
Register μIR
From instruction
register IR
Control Signals
Two Level control store organization for nano programming

## Slide 4: Nanoprogramming
The microprograms are encoded in a narrow vertical format Hm is large Wm is small.
Nano instructions have a highly parallel horizontal format Hm small and Wm large.
If Nanocontrol memory is used it will reduce the total size.
It will provide greater design flexibility.
Nano programming concept was first used in QM-1 computer design
It is also employed in more recent motorolla 68000 series of microprocessors.

## Slide 5: Nanoprogram Control
The nano control memory nCM has a capacity of 1024 nano instructions
The nano instructions are 360 bits long.
Nano instruction addresses are generated by a nano program counter and nano instructions are placed in a register nIR.
The next address of nIR is directly obtained.
The next address is generated by either incrementing the nano program counter or loading it from external source(branch field or address from micro instruction opcode)