## Slide 1: Pipelining
Definition:
Various cycles are involved in instruction cycle. The fetch, decode, Execute and store are performed simultaneously to reduce the overall processing time. This process is called the instruction pipelining

## Slide 2: Pipelining Diagram

## Slide 3: Four-Stage Instruction Pipeline

## Slide 4: Contents
Pipeline stages in MIPS Instruction
Designing instruction set for Pipelining
Pipeline Hazards
Types of Hazards
Pipeline Performance

## Slide 5: Pipeline Stages in MIPS Instruction
Fetch instruction from memory
Read Register and decode the instruction simultaneously
Execute the operation
Access an operand in data memory
Write the result into a register

## Slide 6: Designing Instruction set for Pipelining
All MIPS instructions are same length
MIPS has only a few instruction formats
Operands only appear in load and store instruction
Data can be transferred between processor
and memory in a single pipeline stage

## Slide 7: Pipeline Hazards
Definition:
Any reasons that causes the pipeline to stall is called a Hazard

## Slide 8: Hazards Diagram

## Slide 9: Types of Hazards
Structural Hazards
Data Hazards
Control Hazards or Instruction Hazards

## Slide 10: Structural Hazards
When two instructions require one hardware resource at the same time, the structural hazards will occur

## Slide 11: Data Hazards
The source operand or destination operand are not available at the expected time in the pipeline to run the instructions, the data hazards will occur

## Slide 12: Control Hazards or Instruction Hazards
The Instruction fetch unit supply the instruction stream to the execution unit. The stream is interrupted when pipeline stall occurs due to cache miss or due to branch instruction. This situation is known as Instruction hazard.

## Slide 13: Control Hazards Diagram – Unconditional Branching

## Slide 14: Pipeline Performance